## Slide 1: Coupled “Maxwell-Bloch” - “ensemble Monte Carlo” simulations for THz QCLs
Institute for Nanoelectroncis, Technische Universität München

## Slide 2: Contents
Wave function analysis
  Coupled basis SP calculations (simple 2-well system)
  Tight binding basis SP calculations (simple 2-well system)
  Coupling strength estimation (simple 2 well system)
  Summary of WF analysis for the QCL183S freq comb
Monte-Carlo simulations
  Scattering rates, current and gain estimates
Maxwell-Bloch simulations
  Numerical THz-TDS measurements (ring and FP cavity)
    Dispersion and gain estimates
  Transient dynamics of the investigated device
  Steady state analysis of the lasing spectra at design bias
  Coherence properties of the resulting frequency comb
    SWIFT spectra
    Time-domain spectral analysis/independent comb formation

## Slide 3: Wave function analysis (simple 2Well system)
Decompose original Hamiltonian into a tight-binding Hamiltonian and a residual term ():

## Slide 4: Wave function analysis (simple 2Well system)
Decompose original Hamiltonian into a tight-binding Hamiltonian and a residual term ():

## Slide 5: Wave function analysis (simple 2Well system)
In the full basis two wfs spanning a thick barrier “anticross” with a certain splitting energy .
In such a configuration, electrons tunnel quantum mechanically back and forth between the two separate states across each side of the barrier
To investigate the effect of this “resonant” tunnelling phenomena onto the carrier transport, we employ the TB approximation
In the tight-binding basis the wave functions are localized within a single period -> the electron states in each adjacent period are simply translated in space and energy from the states in the previous period
However the time-evolution of the system is governed by the full Hamiltonian, , where a wave function can span more than one period!
We need to correct for the fact that we are using the tight-binding wave functions by including the correct “coupling” energies in the Hamiltonian.
TB basis wave functions
Coupled basis wave functions

## Slide 6: Wavefunction analysis (simple 2Well system)
Since the TB wavefunctions form a complete basis set we can write down any arbitrary WF of the coupled system as a linear combination
, where the are expansion coefficients and the {} are the eigenstates and eigenenergies of the TB Hamiltonian. Plugging those into the TIDSE:
Multiplying on the right by and performing the integration yields:
Which is a generalized eigenvalue problem

## Slide 7: Wavefunction analysis (simple 2Well system)
In matrix notation we simply get: , where:
A simplistic interpretation of the different integrals is in order:
: is the so called overlap integral, which is in general non-zero for eigenstates spanning a module barrier (since the TB basis states are not necessarily orthogonal to their translated counterparts)
for : is the so called shift integral, which induces a shift in the TB energy level (see fig)
for : is the coupling strength integral, which estimates the overlap between two WFs through a coupling barrier. Namely this term induces the anticrossing/or splitting of two TB eigenstates, initially in resonance. (see fig).
+
-
for – resonance (=)

## Slide 8: Wavefunction analysis (simple 2Well system)
To verify our approach we calculated the wavefunctions in the TB basis, solved the eigenvalue equation:
And calculated the original wavefunctions (on the full basis) with the relation:

## Slide 9: Anticrossings : Extended basis
Strong anticrossing between INJ2 and ULL ( 3.594 meV).
The separation between ULL and LLL1 of approx. 13 meV indicates that LLL1 is the lower laser level. (at same bias the separation between ULL and LLL2 is more than 18 meV – the device does not lase at such a high freq. )
6
7
8
9
10
11
12
13
E
[
m
e
V
]
0
4
8
12
16
18
E
INJ
1
INJ
2
E
INJ
1
ULL
E
INJ
2
ULL
E
ULL LLL
1
E
ULL LLL
2
Bias (kV/cm)
6
7
8
9
10
11
12
13
E
[
m
e
V
]
20
24
28
32
36
40
44
48
E
LLL
1
DEPOP
1
E
LLL
1
DEPOP
2
X: 10.2
Y: 3.594
Active region
Injector
Depop.

## Slide 10: Final model -> tight binding approximation
We took the FL183S AR specification and calculated the wave functions in the tight binding approximation.
40
60
80
100
120
140
160
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
We set up a density matrix model for the full set of energy levels (illustrated in the figure below).
We calculated the different scattering rates (the ’s) with our ensemble Monte Carlo simulator.
We simulated the light-matter coupling via Maxwell-Bloch equations until convergence was reached (approximately 500 round trips are needed for this laser).
Active region
Injector
Depop.

## Slide 11
Rate equations:
Let every electron in |B> be immediately pumped back into |R>
Impose current conservation, i.e.
Carrier Reservoir
Carrier Basin
. . .
Periodic rate equations
A rate equation model that allows us to calculate the current density flowing through the QCL (not along)
Can be easily generalized to a semi-classical approach by incorporating it into the Maxwell-Bloch equations

## Slide 12: Some conventions
In general the E-field is described as ,where is a complex envelope function
Thus for the field spectrum: with
The Maxwell-Bloch equations in the rotating wave approximation & slowly varying envelope approximation write:
, where is the density matrix, the Hamiltonian (which includes also the coupling with the E-field) and contains the scattering rates computed from the Monte Carlo simulations.

## Slide 13
Delay [ps]
-300
-100
0
100
200
300
-200
3.6
3.8
4.0
4.2
4.4
3.4
Frequency [THz]
Simulated spectrum (after 500rt)
and spatial hole burning included
Delay [mm]
-40
-20
0
20
40
1
0
1
1
0
2
1
0
3
1
0
4
1
0
5
3.2
3.4
3.6
3.8
4.0
Frequency [THz]
3.2
3.4
3.6
3.8
4.0
3.0
Frequency [THz]
Experimental spectrum Obtained from: D. P. Burghoff. (2014). Ph.D. dissertation, MIT
3.6
3.8
4.0
4.2
4.4
3.4
Frequency [THz]
Simulation and experiment show broad doubly peaked gain
Unlike experiment, in simulation the two distinct frequency lobes seem to cross-talk (highlighted area) around the central frequency of 3.9 THz.
Time domain data in both experiment and simulation shows an amplitude modulated temporal trace.

## Slide 14: Spectrum analysis:
(Left ) Frequency spectrum of :
  shows equidistantly spaced modes with spacing equal to the RT frequency (approx. 8.2 GHz) . Lowest order mode is namely this frequency.
  Does not show a “dip” as opposed to the THz field spectrum.
  However one can observe a “splitting” of some of the frequency modes (inset) which indicates that two combs with different offset frequency are operating.
(Right) Optical power spectrum.
  Equidistant modes with spacing equal to the RT frequency.
  Strong power loss (dip) in the middle of the spectrum.
  Again one can observe a “splitting” of some of the laser modes (inset) around the central frequency of 3.9 THz.
Freq. (GHz)
240
250
260
270
280
10
0
10
1
10
2
10
3
10
4
Freq. (GHz)
100
200
300
400
500
600
10
-2
10
0
10
2
10
4
10
6
Freq. (THz)
3.88
3.89
3.9
3.91
3.92
10
-2
10
0
10
2
10
4
10
6
10
8

## Slide 15: Time domain analysis:
Time [ps]
140
160
180
200
220
F
r
e
q
.
[
T
H
z
]
3.6
4
4.4
Time [ps]
140
160
180
200
220
I
n
t
e
n
s
i
t
y
[
a
.
u
.
]
0
1
2
(Above) Short time FT spectrogram:
  Spectrogram computed with a hanning window of approx. 5ps
  Shows periodic (with the RT period) alternation of the frequency spectrum from broad to narrow emission
  At the end of every round trip on can observe significant broadening of the spectrum with merging of the high and low freq. lobes.
(Below) Time domain high and low frequency lobe signals.
  Clear periodicity of both signals.
  Alternating broadband and narrowband emission (i.e. short pulses and almost continuous signal) corresponding to the expected behaviour from the spectrogram.