## Slide 1: Coupled “Maxwell-Bloch” - “Ensemble Monte Carlo” simulations for THz QCLs
Institute for Nanoelectroncis, Technische Universität München

## Slide 2: Contents
Wave function analysis
  Coupled basis SP calculations (simple 2-well system)
  Tight binding basis SP calculations (simple 2-well system)
  Coupling strength estimation (simple 2 well system)
  Summary of WF analysis for the QCL183S freq comb
Monte-Carlo simulations
  Scattering rates, current and gain estimates
Maxwell-Bloch simulations
  Numerical THz-TDS measurements (ring and FP cavity)
    Dispersion and gain estimates
  Transient dynamics of the investigated device
  Steady state analysis of the lasing spectra at design bias
  Coherence properties of the resulting frequency comb
    SWIFT spectra
    Time-domain spectral analysis/independent comb formation

## Slide 3: Wave function analysis (TB model)
Decompose original Hamiltonian into a tight-binding Hamiltonian and a residual term ():
The terms and are constructed as graphically depicted below.

## Slide 4: Wavefunction analysis (TB model)
Since the TB wavefunctions form a complete basis set we can write down any arbitrary WF of the coupled system as a linear combination [Bastard1990]
, where the are expansion coefficients to be determined, and {}, {} and {} are the eigenstates and eigenenergies of the TB Hamiltonian , centered at and respectively. Plugging those into the TISE:
Multiplying on the right by and performing the integration yields:
, with similar expressions forand . Let the vector . Then we can rewrite the above expression as a generalized eigenvalue problem:

## Slide 5: Wavefunction analysis (simple 2Well system)
Where and are “nlvl”x”nlvl” submatrices defined by the relations:
… then we can rewrite the above expression as a generalized eigenvalue problem:
A simplistic interpretation of the different integrals is in order:
: is the so called overlap integral, which is in general non-zero for eigenstates spanning a module barrier (since the TB basis states are not necessarily orthogonal to their translated counterparts).
for : is the so called shift integral, which induces a shift in the TB energy level (see fig above).
for : is the coupling strength integral, which estimates the overlap between two WFs through a coupling barrier. Namely this term induces the anticrossing/splitting between two TB eigenstates, initially in resonance (see fig above).
for – resonance (=)
+
-

## Slide 6: Example -> coupled potential wells
To verify our approach we calculated the wavefunctions in the TB basis, i.e. we solved the eigenvalue equation:
.
We then transformed back to the original wavefunctions (the eigenfucntions of ) with the help of the the relation:
.
0
200
400
600
800
1000
0
0.05
0.1
0.15
0.2
0.25
Coupled
0
200
400
600
800
1000
0
0.05
0.1
0.15
0.2
0.25
TB
0
200
400
600
800
1000
0
0.05
0.1
0.15
0.2
0.25
TB->Coupled
z (Angstrom)
z (Angstrom)
z (Angstrom)
E (eV)

## Slide 7: Summary of the modelling of QCL FL183S freq. comb laser
We took the FL183S active region specification and calculated the wave functions in the tight binding approximation.
40
60
80
100
120
140
160
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
We set up a density matrix model for the full set of energy levels (illustrated in the figure below).
We calculated the different scattering rates (the ’s) with our Ensemble Monte Carlo[Jirauschek2014] simulator.
We simulated the light-matter coupling via Maxwell-Bloch equations until convergence was reached (approximately 500 round trips are needed for this laser).
Active region
Injector
Depop.
We performed extensive spectral as well as time domain analysis and obtained considerable agreement with experiment [Burghoff2014,BurhoffPhD,Burghoff2015].

## Slide 8: Wave function analysis (Why the TB approximation?)
In the full basis (or extended basis as found in literature) two WFs spanning a thick barrier “anti-cross” with a certain splitting energy .
In such a configuration, electrons tunnel quantum mechanically back and forth between the two separate states across each side of the barrier [Kumar2009,Callebaut2005].
To investigate the effect of this “resonant” tunnelling phenomena onto the carrier transport, we employ the TB approximation
In the tight-binding model the wave functions are localized within a single period -> the electron states in each adjacent period are simply translated in space and energy from the states in the previous period
However the true time-evolution of the system is still governed by the full Hamiltonian, , where a wave function can span more than one period!
We need to correct for the fact that we are using the tight-binding wave functions by including the correct “coupling” energies in the Hamiltonian matrix.
TB basis WFs
Extended basis WFs

## Slide 9: Maxwell-Bloch equations
Maxwell-Bloch equations: semi-classical description of light matter interaction
Maxwell-Bloch
Maxwell’s equations for the electrical field coupled to Von Neumann equation for the electron states.
The periodic rate equation model (see next slide) is generalized to the density matrix equation via the scattering times matrix .
Maxwell:
Bloch:
Similarly to [Kumar2009], we consider the MB model with a single optical transition and a single INJ->ULL coupling in our Hamiltonian, in effect coherently modelling only 3 of the 7 laser levels. The rest of the levels are included into our density matrix simulation with the corresponding scattering rate equations ONLY. We further perform all calculations in the rotating wave and slowly varying envelope approximations. In the slides to come, we will motivate that our model is agreeable within certain regimes of operation of the laser.

## Slide 10
Periodic rate equations
A rate equation approach that eliminates the need of empirical current pump parameter.
Can be easily generalized to a semi-classical approach by incorporating it within the scattering rates matrix of density matrix equations.
. . .
Carrier Reservoir
Carrier Basin
Rate equations:
Current density:
To illustrate the periodic rate equation model, consider the following discrete system where:
  Current Iin is injected into carrier reservoir level
  Electrons scatter between N channel levels
  Upon reaching the carrier basin level, the electrons are extracted from the system via a Iout current.
To eliminate the current from the rate equations of this system assume:
  Let every electron in |B> be immediately pumped back into |R>, .
  Impose current conservation, i.e. .

## Slide 11: Wavefunction analysis of the gain medium
While the scattering transitions are considered for all levels by the corresponding transition rates, the coherent coupling between injector and upper laser level is only considered for the dominant injection level at the corresponding bias. Similarly, due to the significant difference in oscillator strengths (), we only include the ULL->LLL1 electric field coupling.
INJ1
INJ2
ULL
LLL
INJ1-> ULL resonance
INJ1
INJ2
ULL
LLL
INJ2-> ULL resonance
Since we consider only one injector and only one lower laser level, bias dependent wave function calculations reveal 2 regimes susceptible to our modelling:
@ and around 9.2 kV/cm INJ1->ULL resonance
@ and around 11.0 kV/cm INJ2-> ULL resonance
In both cases we can take as the effective lower laser level, the level denoted by LLL1.
9
9.5
10
10.5
11
11.5
12
0
2
4
6
Z
ULL,LLL1
Z
ULL,LLL2
Energy differences (eV)
E
INJ1,ULL
E
INJ2,ULL
E
INJ1,INJ2
E
ULL,LLL1
E
ULL,LLL2
9
9.5
10
10.5
11
11.5
12
-0.005
0
0.005
0.01
0.015
0.02
0.025
Bias (kV/cm)
0.0009
0.0011
0.0013
0.0015
0.0017
9
9.5
10
10.5
11
11.5
12
X: 9.2
Y:0.01348
(anticrossing
Strengths) (eV)
X: 9.2
Y:-0.004419
X: 9.2
Y:0.001572
X: 9.2
Y:0.009638
X: 11
Y:0.01606
X: 11
Y:0.004335
X: 11
Y:0.001384
X: 11
Y:0.001184
X: 11
Y:4.439
X: 11
Y:0.4136
X: 9.2
Y:2.393
X: 9.2
Y:0.6656
(dipole mtx
elements) (nm)

## Slide 12: Scattering times matrices
Used Monte Carlo simulations to extract the scattering times between all different laser levels at 10.8 kV/cm , 11.0 kV/c, and 11.2 kV/cm biases. Due to the fact that the WFs are calculated in the TB approximation, one can determine INTER-module and INTRA-module scattering rates. We assume that in the real system the transport trough the barrier is governed by resonant tunneling.
The scattering times between for different bias levels are as follows (in units of picosecond)
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1.2 | 1.3 | 56.5 | 748.2 | 1608.4 | 471.1 | 512.4
2 | 2.1 | 1.8 | 15 | 554.3 | 1518.8 | 551.5 | 502.7
3 | 27.4 | 8.2 | 2.1 | 7.5 | 9.8 | 20.3 | 22.9
4 | 41.5 | 35.9 | 12.9 | 0.5 | 2.1 | 1.3 | 1.8
5 | 83.8 | 51.3 | 32.4 | 3.6 | 0.4 | 0.9 | 0.9
6 | 512.9 | 372.3 | 318.3 | 268.2 | 181.1 | 1.3 | 1.3
7 | 844.7 | 579 | 533.8 | 691.4 | 219.2 | 2.1 | 0
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1.2 | 1.3 | 47.6 | 550.2 | 1281 | 368.8 | 404.6
2 | 2.1 | 1.8 | 16.5 | 467.8 | 1140.8 | 380.3 | 351.6
3 | 22.7 | 10.5 | 2.1 | 7.1 | 10.1 | 20.6 | 24.6
4 | 33 | 24.1 | 11.6 | 0.5 | 2.1 | 1.4 | 2.1
5 | 55.2 | 33.9 | 34 | 3.6 | 0.4 | 0.8 | 0.9
6 | 403.9 | 283 | 300.2 | 274 | 156.4 | 1.3 | 1.3
7 | 619.8 | 400.9 | 481.5 | 852.3 | 229.9 | 2.1 | 0
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1.2 | 1.2 | 49.9 | 611.3 | 1487.8 | 396.1 | 341.4
2 | 2 | 1.9 | 22.2 | 641.2 | 1469.6 | 415.6 | 327.3
3 | 21.2 | 11.2 | 2.1 | 8 | 9.1 | 19.9 | 21.5
4 | 30.4 | 23.5 | 12.6 | 0.5 | 2 | 1.3 | 1.6
5 | 46.7 | 35.7 | 28 | 3.6 | 0.4 | 1 | 0.9
6 | 387.3 | 272.2 | 343.1 | 317.6 | 235.6 | 1.2 | 1.2
7 | 598.9 | 392.2 | 552.6 | 762.7 | 240.1 | 2 | 0
11.2 kV/cm
11.0 kV/cm
10.8 kV/cm
The ordering in the table is the following:
INJ1 <-> 1
INJ2 <-> 2
ULL <-> 3
LLL1 <-> 4
LLL2 <-> 5
DEPOP1 <-> 6
DEPOP2 <-> 7
Since DEPOP2 is considered as the “Carrier Basin level” , its effective lifetime is 0.
For the pure dephasing, we consider for the INJ-> ULL transition and for the rest of the transitions [DUPONT2010].

## Slide 13: Gain analysis
Numerical TDs Measurements [BurghoffPhD]
Seed THz pulse: an unchirped Gaussian pulse, centered at f_0, with a bandwidth of approx. 2 THz.
TODO:NOTE IF YOUR SEED PULSE IS NOT TOO STRONG!
Output pulse after light has propagated for 3 roundtrips inside a 1.5 mm long RING cavity.
The gain is estimated by the ratio of the amplitudes of the output and seed field’s spectral components, and respectively, via:
  G(w) =)
• At resonance (kV/cm ): formation of two equally strong frequency lobes.
• Below resonance (): high frequency lobe dominates.
• Above resonance (): low frequency lobe dominates.
In published experimental data [BurghoffPhD] the current was fixed so direct comparison is difficult, however our results agree with previously published theoretical results [Dupont2010].
10.8 kV/cm
11.2 kV/cm
11.0 kV/cm
Net amplitude gain (1/cm)
Frequency (THz)
2.5
3
3.5
4
4.5
5
5.5
-4
-2
0
2
Time (ps)
0
5
10
15
-5
0
5
11.2 kV/cm
Time (ps)
0
5
10
15
-5
0
5
Time (ps)
0
5
10
15
-5
0
5
11.0 kV/cm
Time (ps)
0
5
10
15
-5
0
5
Time (ps)
0
5
10
15
-5
0
5
Time (ps)
0
5
10
15
-5
0
5
10.8 kV/cm
Seed field (a.u.)
Out-field (a.u.)

## Slide 14
Spectral analysis
Simulations until steady state has been reached for three different bias levels: 10.8, 11.0 and 11.2 kV/cm below at and above resonance, respectively.
We assumed a 5mm long FP cavity with perfectly reflecting mirrors, where light propagates in a medium with an effective refractive index of . The lifetimes of the different levels together with the dephasing life-times are mentioned in the slide on Monte-Carlo simulations. Total power losses (waveguide+reflection losses) considered are 20.
Spectral measurements were averaged over approximately 400 round trips or approximately 47 ns, which yields spectral resolution of:
19 MHz
with a bandwidth of
20 THz.
We observed two general tendencies:
Blueshift of the central frequency (f0) with increasing bias levels
Shift of the dominant component of the gain from the high to low frequency lobe (again with increasing bias levels) -> in agreement with numerical THz TDS simulations.
4.5
Freq. (THz)
3.5
4
10.8 kV/cm
4.5
3.5
4
Freq. (THz)
11.2 kV/cm
Freq. (THz)
3.5
4
4.5
11.0 kV/cm
Optical power (a.u.)
Optical power (a.u.)
Optical power (a.u.)

## Slide 15
Correlation
Spectrum product
3.4
3.6
3.8
4
4.2
4.4
SWIFT @11 kV/cm
Spectral analysis (2)
SWIFT [Burghoff2014] analysis was also conducted, averaged over a signal with duration 47ns, overlapped with a Hamming window apodization function.
The significant overlap between the correlation spectrum and the spectrum product indicate almost perfect coherence of the spectral comb lines -> possibly due to the neglected waveguide group velocity dispersion (the only dispersion assumed is the three level quantum system dispersion).
According to theory [Burghoff2015], the correlation spectrum is correctly upper bounded by the spectrum product, as also seen in the simulation (inset).

## Slide 16
Time-domain analysis
The time-domain signal was bandpass filtered (below and above the central frequency) with two FIR filters of order 100, with a constant delay and magnitude response function as depicted in the figure below:
Normalized Frequency (
rad/sample)
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
0.4
-60
-40
-20
0
Magnitude Response (dB)
Magnitude (dB)
The filtered electric field data was then corrected for group delay and plotted versus time.
A clear switching between high and low frequency lobe pulses can be observed!
Field Intensity (a.u.)
Field Intensity (a.u.)
Field Intensity (a.u.)
In effect -> one of the signals acts as a “saturable absorber” to the other and the difference in duration of the corresponding pulses seems to increase with increasing asymmetry between the high and low frequency gain components.
-200
-150
-100
-50
0
50
100
150
200
0
5
10
10.8 kV/cm
-200
-150
-100
-50
0
50
100
150
200
0
5
10
11.0 kV/cm
Low Freq. Lobe
High Freq. Lobe
-200
-150
-100
-50
0
50
100
150
200
0
5
10
11.2 kV/cm

## Slide 17
Interferometric Autocorrelation
Field Autocorrelation
Time (ps)
Time (ps)
Time-domain analysis 10.8 kV/CM
2xRT freq
The short time Fourier transform of the electric field (with Hamming window of approximately 5ps) reveals gain switching between high and low freq. lobe components.
The gain switching corresponds to high/low freq. lobe pulse formation, with a more pronounced high frequency lobe pulse (as expected from Gain analysis).
Calculated current oscillates around a mean value of 832 A/cm2 with each peak in phase with gain switching
DFT transform of the current reveals (besides the strong DC signal), strong components at an integer multiple of the RT frequency -> strongest of which is 2xRT freq.
Interferometric AC result -> “Peek to background” (P2B) ratio of 8:1 for the low freq. lobe and (P2B) of 8:2 for the high frequency lobe signal.
4)
3)
2)
1)
5)
P2B: 8:1
P2B: 8:2
Low Freq. Lobe
High Freq. Lobe
TODOS:
HOW DO THE P(w)^2 spectra compare with the J(w) spectra??
Investigate regimes of operation where one can observe DOUBLING of the mode spacing !
It seems that 1000 RT do not suffice for convergence to be reached. Simulate for 5000 RTs?

## Slide 18
Interferometric Autocorrelation
Field Autocorrelation
Time (ps)
Time (ps)
Time-domain analysis 11.0 kV/CM
2xRT freq
At resonance the gain switching is more equally distributed between the two different freq. lobes .
The pulse duration of both field components is approximately the same .
Calculated current oscillates around a mean value of 819 A/cm2 with each peak in phase with gain switching
DFT transform of the current reveals a strong signal at 2xRT frequency -> current responds to the arrival of the two different freq. lobe pulses.
Interferometric AC result -> two pulses with P2B ratio of 8:1 .
4)
3)
2)
1)
5)
P2B : 8:1
P2B: 8:1
Low Freq. Lobe
High Freq. Lobe
TODOS:
HOW DO THE P(w)^2 spectra compare with the J(w) spectra??
Investigate regimes of operation where one can observe DOUBLING of the mode spacing !
It seems that 1000 RT do not suffice for convergence to be reached. Simulate for 5000 RTs?

## Slide 19
Interferometric Autocorrelation
Field Autocorrelation
Time (ps)
Time (ps)
Time-domain analysis 11.2 kV/CM
1xRT freq
4)
3)
2)
1)
5)
P2B: 8:2
P2B: 8:1
Low Freq. Lobe
High Freq. Lobe
Above resonance the low frequency lobe dominates the spectrum.
The intensities of both lobes are again equal in strength but the low frequency lobe is longer in duration.
Calculated current oscillates around a mean value of 794 A/cm2 which is smaller than the value at resonance bias of 11kV/cm -> simulated laser seems to be in a NDR regime.
Frequency spectrum of the current shows a strong component at the RT frequency.
Interferometric AC result -> again P2B ratios of 8:2 and 8:1 for the different frequency lobes.
TODOS:
HOW DO THE P(w)^2 spectra compare with the J(w) spectra??
Investigate regimes of operation where one can observe DOUBLING of the mode spacing !
It seems that 1000 RT do not suffice for convergence to be reached. Simulate for 5000 RTs?

## Slide 20: References
[Dupont2010] E. Dupont, S. Fathololoumi and H.C. Liu ,” Simplified density-matrix model applied to three-well terahertz quantum cascade lasers”, Phys. Rev B 81 (2010) .
[Burghoff2014] David Burghoff, Tsung-Yu Kao, Ningren Han, Chun Wang Ivan Chan, Xiaowei Cai, Yang Yang, Darren J. Hayton, Jian-Rong Gao, John L. Reno and Qing Hu , “Terahertz laser frequency combs”, Nat. Phot. 8 (2014).
[Jirauschek2014] Christian Jirauschek, Tillmann Kubis, “Modeling techniques for quantum cascade lasers”, Appl. Phys. Rev. 1 (2014).
[Burghoff2015] David Burghoff, Yang Yang, Darren J. Hayton, Jian-Rong Gao, John L. Reno, and Qing Hu “Evaluating the coherence and time-domain profile of quantum cascade laser frequency combs” , Opt. Exp. 1190 (2015).
[BurghoffPhD] D. P. Burghoff. (2014). Ph.D. dissertation, MIT.
[Bastard1990] G. Bastard, “Wave Mechanics Applied to Semiconductor Heterostructures”, Les Éditions de Physique, Les Ulis, France, 1990.
[Kumar2009] Sushil Kumar and Qing Hu, “Coherence of resonant-tunneling transport in terahertz quantum-cascade lasers” , Phys. Rev. B 80 (2009).
[Callebaut2005] Hans Callebaut and Qing Hu, “Importance of coherence for electron transport in terahertz quantum cascade lasers”, J. Appl. Phys. 98 (2005)